## Slide 1: NSCAP @CS.NCTU
Lab6: OFDM Simulation
Instructor: Kate Lin

## Slide 2: Source Code
SISO OFDM: https://warpproject.org/trac/browser/ResearchApps/PHY/WARPLAB/WARPLab7/M_Code_Examples/wl_example_siso_ofdm_txrx.m
  Set USE_WARPLAB_TXRX = 0;
Generate frequency-domain channels and noise
  Call h_gen(yourID)to generate the input file input.mat (simulated channels and noise vector)
  Note: we will test your code using a different seed and different SNR configurations. However, your report should be written using the input generated by h_gen(yourID)

## Slide 3: Tasks (code)
Load the channel state information and noise vector from input.mat
  H(1:32) is the channel of subcarriers (0:31) while H(33:64) is the channels of subcarriers of (-32:-1)
Apply the frequency domain channel
  Just apply H(i) to data point X(i)
Add the noise vector, n_vec, to the time-domain signals
Calculate the average SNR(dB) of each data subcarrier (16QAM)
Calculate the average SNR(dB) of all the data subcarriers
Calculate the bit error rate of each subcarrier (16QAM)
Try different modulations and output the throughput of the optimal modulation
  symbol duration is 4us, no coding scheme

## Slide 4: Tasks (report)
Output the estimated frequency channels of data subcarriers
Plot the power of channel responses of the data subcarriers and output which one experiences the minimum receiving power
  X-axis: index of subcarrier, y-axis: |H|2
Output the average SNR(dB) of each subcarriers (16QAM)
Output the average SNR(dB) of all the data subcarrier (16QAM)
Output the bit-error rate of each subcarrier (16QAM)
Plot the throughput of each modulation
  X-axis: modulation, y-axis: throughput
Plot the constellation diagram of 16QAM and mark the erroneous sample as the green dots

## Slide 5: Submission
Upload your files to E3
  Report: report_(yourID).pdf, e.g., report_111111.pdf
  Code: wl_example_siso_ofdm_txrx_(yourID).m

## Slide 6: Grading Policy
Deadline – 2022.05.22 23:59 (by Sunday night)
Grade
  code correctness - 40%
  Report - 60%
Late Policy
  (Your score ) * 0.8D, where D is the number of days over due
Cheating Policy
  Academic integrity: Homework must be your own – cheaters share the score
  Both the cheaters and the students who aided the cheater equally share the score