## Slide 1: NSCAP @CS.NCTU
Project Checkpoint#1: OpenWrt Installation
Instructor: Kate Lin

## Slide 2: Objectives
In this checkpoint, we are going to install OpenWrt on router, and setup the wifi on it You’ll learn:
  How to build OpenWrt images
  How to install OpenWrt
  How to setup Wi-Fi in OpenWrt

## Slide 3: Intro. to OpenWrt

## Slide 4: OpenWrt
A Linux Distribution designed for embedded devices to route network traffic
Lots of software packages are available for installation, providing network functions that are not supported by stock firmware

## Slide 5: Tasks

## Slide 6: Tasks
Building OpenWrt images
  [Method 1] Self-compile (Build system)
  [Method 2] Using the Image Builder
Install OpenWrt via Edimax router’s web UI
Enable and configure Wi-Fi
  [Method 1] Using terminal
  [Method 2] Using web UI
Configure WAN (optional)
  [Method 1] Using terminal
  [Method 2] Using web UI

## Slide 7: Build OpenWrt Images
Self-compile (Build system)

## Slide 8: Environment
Install the virtual machine (if necessary)
Recommended specifications of VM
  OS: Ubuntu 20.04
  CPU: 2 up
  RAM: 4GB up
  Disk size: 40GB up
If you don’t satisfied the recommended spec, you can try to use GitHub Actions as your build environment

## Slide 9: Build Images
Install building dependencies
  # sudo apt update
  # sudo apt install build-essential\ ccache ecj fastjar file g++ gawk\ gettext git java-propose-classpath\ libelf-dev libncurses5-dev\ libncursesw5-dev libssl-dev python\ python2.7-dev python3 unzip wget\ python3-distutils python3-setuptools\ python3-dev rsync subversion swig time\ xsltproc zlib1g-dev

## Slide 10: Build Images
Clone OpenWrt project, select the latest release version, update building feeds, and get default building config for ramips/mt7620 series
  # git clone\ https://git.openwrt.org/openwrt/openwrt.git
  # cd openwrt
  # git pull
  # git branch –a --- Check all branches
  # git checkout --track\ origin/openwrt-21.02 --- Optional

## Slide 11: Build Images
Cont’d
  # git tag --- Check all tags (release version)
  # git checkout v21.02.2
  # ./scripts/feeds update –a &&\ ./scripts/feeds install –a
  # wget\ https://downloads.openwrt.org/releases/21.02.2/targets/ramips/mt7620/config.buildinfo -O .config ---Download config file

## Slide 12: Build Images
Setup building config
  # cd ~/openwrt
  # make menuconfig

## Slide 13: Build Images
After setting up building config, you will enter the appearance below

## Slide 14: Build Images
Load default config for ramips/mt7620 series first
  Use left and right arrow to highlight < Load >, and then press enter to select
  Press enter again to load the config
  Now
--- Target System should be MediaTek Ralink MIPS
--- Subtarget should be MT7620 based boards
Change target profile to Edimax BR-6478AC V2
  Use up and down arrow to highlight Target Profile, and then press enter to select
  Use up and down arrow to highlight Edimax BR-6478AC V2, and then press space to select

## Slide 15: Build Images
Deselect following packages to save more space
  (N) LuCI → Collections → luci-ssl
  (N) LuCI → Collections → luci
  (N) LuCI → Protocols → luci-proto-ipv6
  (N) LuCI → Protocols → luci-proto-ppp
  (N) Libraries → rpcd-mod-rrdns
  (N) Network → Firewall → ip6tables
  (N) Network → odhcp6c
  (N) Network → odhcpd-ipv6only
  (N) Network → ppp-mod-pppoe
  (N) Network → ppp
  (N) Utilities → Encryption → px5g-wolfssl
  (N) Utilities → iwinfo

## Slide 16: Build Images
Select following packages
  (Y) Network → Open vSwitch → openvswitch
Change image distribution name to proof that this image is self-compile
  Image configuration → Version configuration options → Release distribution
    Change it from “OpenWrt” to your student id number
Save & Exit
Build the image
  # make -j $(nproc) defconfig download\ clean world

## Slide 17: Find your image
Once you complete the building process, you can find your image in following location
  /home/nscap/openwrt/bin/targets/ramips/mt7620/ <student id>-21.02.2-ramips-mt7620-edimax_br- 6478ac-v2-squashfs-sysupgrade.bin

## Slide 18: Build OpenWrt Images
Using the Image Builder

## Slide 19: Build Images
Recommended disk size for VM : 50GB
Install building dependencies
  # sudo apt update
  # sudo apt install build-essential\ libncurses5-dev libncursesw5-dev \
  zlib1g-dev gawk git gettext libssl-dev\ xsltproc rsync wget unzip python

## Slide 20: Build Images
Download image builder
  # wget\ https://downloads.openwrt.org/releases/21.02.2/targets/ramips/mt7620/openwrt-imagebuilder-21.02.2-ramips-mt7620.Linux-x86_64.tar.xz
  --- Download mt7620 series image builder
  # tar Jxvf\ openwrt-imagebuilder-21.02.2-ramips-mt7620.Linux-x86_64.tar.xz
  --- Decompress the downloaded file

## Slide 21: Build Images
Build the image
  # make image PROFILE=edimax_br-6478ac-v2 PACKAGES="-ppp-mod-pppoe -ppp -odhcp6c -ip6tables -odhcpd-ipv6only -kmod-pppoe -kmod-ip6tables uhttpd uhttpd-mod-ubus luci-mod-admin-full luci-app-firewall luci-app-opkg luci-theme-bootstrap openvswitch"

## Slide 22: Find your image
Once you complete the building process, you can find your image in following location
  /home/nscap/openwrt/bin/targets/ramips/mt7620/ openwrt-21.02.2-ramips-mt7620-edimax_br-6478ac-v2-squashfs-sysupgrade.bin

## Slide 23: Install OpenWrt

## Slide 24: Install OpenWrt
Connect to Edimax via Wi-Fi or ethernet
Login to Edimax web UI
  http://192.168.1.1
  Account/Password: check manual

## Slide 25: Install OpenWrt
Use Edimax web UI’s upgrade tool to install OpenWrt

## Slide 26: Enable and Configure Wi-Fi
Using Terminal

## Slide 27: Enable and Configure Wi-Fi
Connect to the router via ethernet
  Since Wi-Fi is disabled by default after you do a fresh install of OpenWrt
Login to OpenWrt via SSH using your computer
  # ssh root@192.168.1.1
  Contact TA if you have waited for 10 mins and still can’t ssh into it
Change root’s password first
  # passwd

## Slide 28: Enable and Configure Wi-Fi
Enable 2.4GHz/5GHz Wi-Fi
  # vim /etc/config/wireless
  Change config file like below:
5Ghz
2.4Ghz
Remove this line to enable Wi-Fi
Remove this line to enable Wi-Fi

## Slide 29: Enable and Configure Wi-Fi
Enable 2.4GHz/5GHz Wi-Fi
  # vim /etc/config/wireless
  Change config file like below:
5Ghz
2.4Ghz
Set Wi-Fi’s SSID
Set Wi-Fi’s password
Set encryption method (psk2 means WPA2)
Set Wi-Fi’s SSID
Set Wi-Fi’s password
Set encryption method (psk2 means WPA2)

## Slide 30: Enable and Configure Wi-Fi
Restart Wi-Fi
  # wifi
  You can find your AP and connect to it

## Slide 31: Enable and Configure Wi-Fi
Using Web UI

## Slide 32: Enable and Configure Wi-Fi
Connect to the router via ethernet
  Since Wi-Fi is disabled by default after you do a fresh install of OpenWrt
Login to OpenWrt web UI
  http://192.168.1.1
  Username/Password: root/root
Change admin’s password first
  Goto System -> Administration

## Slide 33: Enable and Configure Wi-Fi
Enable 2.4GHz/5GHz Wi-Fi
  Goto System -> Wireless
  Click Enable
5Ghz
2.4Ghz

## Slide 34: Enable and Configure Wi-Fi
Configure 2.4GHz/5GHz Wi-Fi
  Click Edit
    ESSID: <router’s name>

## Slide 35: Enable and Configure Wi-Fi
Configure 2.4GHz/5GHz Wi-Fi (cont.)
  Click Wireless Security
    Encryption: WPA2-PSK
    Key: <router’s password>
  Click Save&Apply

## Slide 36: Configure WAN (optional)
Using Terminal

## Slide 37: Configure WAN (optional)
If your gateway router use DHCP, then you can skip this part
Otherwise, we have to manually configure IP address on our router

## Slide 38: Configure WAN (optional)
After you ssh into the AP, you can
  # vim /etc/config/network
  Change config file like below:
“eth0.2” is the WAN port behind the router
Set proto to “static” means you want to use static IP
Set your netmask
Set your DNS (this is optional)
Set your static IP address
Set your gateway
IPv4

## Slide 39: Configure WAN (optional)
There’s also an interface in /etc/config/network called “wan6” for IPv6
Reload Network
  # /etc/init.d/network reload

## Slide 40: Configure WAN (optional)
Using Web UI

## Slide 41: Configure WAN (optional)
If your gateway router use DHCP, then you can skip this part
Otherwise, we have to manually configure IP address on our router

## Slide 42: Configure WAN (optional)
Goto Network -> Interfaces
  Click Edit
    Protocol: Static address
  Click Switch Protocol
IPv4
IPv6

## Slide 43: Configure WAN (optional)
Configure WAN
  Protocol: Static address
  Click Switch Protocol
  Configure following attributes by yourself

## Slide 44: Configure WAN (optional)
Your mobile devices can now access Internet via your OpenWrt router :-)

## Slide 45: Submission

## Slide 46: Grading Policy
Report(100%)
Building images (50%)
Use self-compile or image builder (only get 70% of score in this part if using image builder)
Briefly explain the process to complete this part
Screenshots
2. Install OpenWrt (20%)
Screenshots
3. Enable and Configure Wi-Fi (or WAN) (20%)
  Screenshots
4. Thoughts on this Project (10%)
Difficulties encountered
Suggestion if any

## Slide 47: Screenshots
Please providing at least the following screenshots :
  The welcome screen after ssh to router
  The result after execute the following command
# ovs-ctl -V
# ubus call system board
# wifi status
# ping 8.8.8.8
“respectively…”
Please take screenshots by yourself (Do not directly take what we provided or using classmates’)

## Slide 48: Reference
https://openwrt.org/docs/guide-developer/toolchain/beginners-build-guide
https://openwrt.org/docs/guide-developer/toolchain/install-buildsystem
https://openwrt.org/docs/guide-user/additional-software/saving_space
https://openwrt.org/docs/guide-user/additional-software/imagebuilder
https://openwrt.org/docs/guide-developer/toolchain/use-buildsystem
https://openwrt-nctu.gitbook.io/project/
https://upsangel.com/openwrt/openwrt-beginner-guide/
https://zh.wikipedia.org/wiki/OpenWrt